## Slide 1
Thermomechanical Co-Design of TIM1
FINAL COMPETITION PRESENTATION
Interface-Aware Thermal
Interface Material Optimization
A representative 700-W AI accelerator FCBGA package
THERMAL + MECHANICAL
CONTACT GEOMETRY
Fang Tianchi · Ke Tangxin · Du Yanzhang · Duan Yihe
EPTC 2026 Student Innovation Challenge | Singapore
KEY DESIGN DECISION
100 µm
vs 250 µm
The coolest TIM is not always the mechanically least loaded.
Matched nine-case DOE
Source: team simulation study and the supplied EPTC 2026 competition report.
1

## Slide 2
Why TIM1 becomes the design bottleneck
RESEARCH PROBLEM
Published TIM context: Prasher (2006); Due & Robinson (2013); Zhao et al. (2019).
High power density
A nonuniform 700-W die load creates severe thermal demands for the die-to-lid interface.
Real interfaces are imperfect
Bulk k alone misses compressed BLT, contact resistance, partial retention and local gaps.
Reliability is multiphysics
Thinner or stiffer interfaces can change stress and strain even when warpage improves.
The optimization target is package behavior—not a single nominal material property.
2

## Slide 3
Research questions and objectives
OBJECTIVES
Literature: Yi et al. (2025); Wen et al. (2026); Prasher (2006). Source details on references slide.
01
THERMAL
How do TIM family, k and BLT affect the modeled die temperature?
02
INTERFACE
How much does retained contact geometry matter beyond retained area?
03
MECHANICAL
Does the best thermal design also reduce TIM stress, strain and lid warpage?
04
DECISION
Which sampled candidates deserve experimental qualification?
3

## Slide 4
An evidence-led optimization workflow
METHODS
Source: project Icepak/MAPDL numerical results; 23 Oct 2026 evidence freeze. Model-specific, not experimental data.
1
Analytical model
Bulk resistance & assumptions
2
Icepak FEA
Materials, coverage, k–BLT DOE
3
Numerical gates
Baseline replication & mesh checks
4
MAPDL mechanics
One-way, fully bonded handoff
5
Design decision
Thermal vs. stress/strain/warpage
All curves and design comparisons use solved cases—not an inferred lifetime or fabricated optimum.
4

## Slide 5
Representative FCBGA package model
METHODS / MODEL
Copper lid / TIM2 / substrate: Wen et al., Int. J. Therm. Sci. 221 (2026), 110432. DOI: 10.1016/j.ijthermalsci.2025.110432. Die, cooler thickness and 700 W: study-defined.
Fixed-temperature cold plate
60 × 60 × 8 mm • top at 25 °C
TIM2
0.10 mm • k = 5.4 W/(m·K)
Copper lid
52.4 × 52.4 × 0.70 mm
TIM1 — the design variable
k, BLT and contact area
Silicon die
28.5 × 28.5 × 0.70 mm • 700 W
Equivalent support / substrate
52.4 × 52.4 × 1.0 mm
Schematic only • Not a proprietary accelerator geometry • One-way thermal-to-mechanical coupling
5

## Slide 6
Dimensions and literature: what came from where
METHODS / PARAMETER PROVENANCE
Wen et al., Int. J. Therm. Sci. 221 (2026), 110432. DOI: 10.1016/j.ijthermalsci.2025.110432. Yi et al., Microelectron. Reliab. 166 (2025), 115607. DOI: 10.1016/j.microrel.2025.115607.
Package element
Modeled input
Source classification
Copper lid
52.4 × 52.4 × 0.70 mm
Wen et al. (2026), cited DOI
TIM2
0.10 mm; 5.4 W/(m·K)
Wen et al. (2026), cited DOI
Equivalent substrate
52.4 × 52.4 × 1.0 mm
Literature-aligned, Wen et al.
Carbon thermal anchor
21 W/(m·K); 88.22 / 64.82% area
Yi et al. (2025), cited DOI
Die + imposed power
28.5 mm die; 700 W, 4 × 4 map
Study-defined—not measured
Cold plate / boundary
60 × 60 × 8 mm; fixed 25 °C
Footprint literature-aligned; rest assumed
Design variables
k = 15/21/30; BLT = 100/250/400 µm
Simulation DOE, not a vendor specification
DOIs: Wen 10.1016/j.ijthermalsci.2025.110432; Yi 10.1016/j.microrel.2025.115607
6

## Slide 7
Model assumptions: documented, not disguised
METHODS / TRACEABILITY
TIM conductivity / coverage: Yi et al., Microelectron. Reliab. 166 (2025), 115607. DOI: 10.1016/j.microrel.2025.115607. Geometry anchors: Wen et al., Int. J. Therm. Sci. 221 (2026), 110432. DOI: 10.1016/j.ijthermalsci.2025.110432.
Literature-anchored
21 W/(m·K) carbon pad; 88.22% and 64.82% contact fractions
Literature-aligned
52.4 mm substrate and lid; 0.1 mm TIM2; 60 mm cooler footprint
Study-defined
700-W, 4×4 hotspot map; 28.5 mm die; 25 °C fixed boundary
Sensitivity variables
k = 15/21/30; BLT = 100/250/400 µm; carbon effective modulus/CTE
Neither the 700 W heat map nor k = 30 W/(m·K) at 100 µm has been measured on a product.
7

## Slide 8
Thermal resistance: more than bulk conductivity
PHYSICAL MODEL
Thermal contact formulation: Prasher (2006), DOI: 10.1109/JPROC.2006.879796; Zhao et al., Int. J. Heat Mass Transfer 140 (2019), 705-716. DOI: 10.1016/j.ijheatmasstransfer.2019.06.045.
Intrinsic bulk contribution
R_bulk ≈ BLT / (k⊥ × A)
Reducing BLT or increasing k lowers the ideal layer resistance.
Installed interface contribution
R ≈ R_c,die + BLT/(k⊥ A_eff) + R_c,lid
Real contact adds pressure-, surface- and temperature-dependent effects.
Reported metric: R_eff = (peak die temperature − 25 °C) / 700 W
8

## Slide 9
Why begin with a 45-W analytical model?
RESEARCH METHOD / FOUNDATION
Source: team's 45-W X23 verification and mesh logs; the 0.200 °C/W reference was study-selected.
First establish a controlled heat path before simulating a 700-W accelerator.
Analytical expectation
Rbulk = 0.115385 °C/W
45 W through the reference X23 TIM gives ~5.192 °C bulk drop.
Numerical convergence
0.000387%
Medium-to-fine change in die peak temperature; mesh refinement alone was stable.
Calibration limitation
27.72%
FEA reference resistance 0.144568 °C/W versus selected 0.200 °C/W comparison target.
Why it mattered: detect model/interface assumptions before comparing materials under 700 W.
9

## Slide 10
What the initial verification did—and did not—establish
RESEARCH METHOD / INTERFACE VALIDITY
Source: team's separate 45-W analytical, mesh and calibration diagnostic; not a physical contact measurement.
Model observation
Analytical layer resistance and FEA package resistance are different quantities.
The mesh check was stable; agreement with an external target was not established.
The mismatch motivated separating bulk and interface contributions.
Scope of the subsequent study
An 8.65 °C·mm²/W effective fitting term was explored in a separate diagnostic.
It was NOT transferred to the 700-W material and DOE simulations.
Consequently, the main comparisons use ideal thermal interfaces.
Interpret the subsequent temperatures as model-specific comparative results, not qualified junction temperatures.
10

## Slide 11
Constructed 4 × 4 die power map
METHODS / THERMAL LOAD
Source: project Icepak/MAPDL numerical results; 23 Oct 2026 evidence freeze. Model-specific, not experimental data.
7 W
42 W
42 W
7 W
42 W
84 W
84 W
42 W
42 W
84 W
84 W
42 W
7 W
42 W
42 W
7 W
700 W total
4 central tiles × 84 W = 336 W
8 adjacent tiles × 42 W = 336 W
4 corner tiles × 7 W = 28 W
A fixed, nonuniform load reveals why contact loss beneath hotspots can be critical.
11

## Slide 12
Numerical credibility and verification gates
METHODS / VALIDATION
Source: project Icepak/MAPDL numerical results; 23 Oct 2026 evidence freeze. Model-specific, not experimental data.
0.256%
Grease medium-to-fine ΔTmax
<0.004 °C
Independent carbon reproduction
0.000031 °C
DOE control-point difference
What these checks do — and do not — prove
These are numerical consistency checks—not experimental calibration. The later 700-W study assumes ideal thermal contact.
12

## Slide 13
Baseline comparison: grease, carbon and indium
RESULTS / MATERIAL SCREEN
Project 700-W simulation. Materials have different k and BLT—this is a screen, not an isolated k effect.
Grease • 5 / 90 µm
102.534°C
Carbon • 21 / 250 µm
93.344°C
Indium • 86 / 400 µm
81.883°C
−9.19 °C
Carbon vs. grease
−20.65 °C
Indium vs. grease
Nominal ideal contact
13

## Slide 14
Why a thermal material screen was not enough
RESEARCH PROGRESSION / INITIAL MECHANICS
Team's MAPDL grease/indium results; indium constitutive sensitivity is a study assumption, not fatigue prediction.
Thermal benefit did not establish the mechanically preferable TIM.
COMPLIANT GREASE
0.00105 MPa
Mean modeled TIM stress; assumed E = 0.05 MPa. Warpage ≈ 15.51 µm.
ELASTIC INDIUM
50.90 MPa
Elastic mean stress is not credible as a realistic post-yield service prediction.
PLASTICITY SENSITIVITY
0.51% / 0.49%
Mean plastic strain at assumed 1.00 / 2.14 MPa yields; no lifecycle prediction.
Reason for the next step: use carbon design variables and a consistent mechanical model.
14

## Slide 15
Contact retention affects hotspot temperature
RESULTS / INTERFACE RETENTION
Published retained-area fractions only: Yi et al., Microelectron. Reliab. 166 (2025), 115607. DOI: 10.1016/j.microrel.2025.115607. Thermal temperatures: team's simulations.
100%
93.3°
88.22%
93.7°
64.82%
109.8°
Important distinction
Yi et al.: measured coverage ratios
Here: assumed missing-contact shapes
Not a measured failure progression
The 88.22% retained-area case changes little; a more severe 64.82% ring loss changes much more.
15

## Slide 16
Equal coverage does not imply equal heat removal
RESULTS / CONTACT TOPOLOGY
Project topology scenarios at 64.82% area; severe conductive blockage, not physical aging predictions.
Peripheral ring
109.8 °C
One edge band
417.8 °C
Central void
400.5 °C
All three scenarios assume 64.82% retained TIM1 area; topology sketches are illustrative.
Coverage fractions: Yi et al., Microelectron. Reliab. 166 (2025), 115607. DOI: 10.1016/j.microrel.2025.115607. Spatial loss maps and all temperatures: study-defined simulations.
16

## Slide 17
The full 3 × 3 conductivity–thickness thermal DOE
RESULTS / NINE SOLVED CASES
Team's nine Icepak simulations; parameter plausibility: Li et al., Compos. Sci. Technol. 234 (2023), 109948. DOI: 10.1016/j.compscitech.2023.109948.
100 µm
250 µm
400 µm
k = 15
85.490
100.323
114.389
k = 21
82.625
93.344
103.544
k = 30
80.455
88.026
95.194
THERMAL BEST
80.455 °C
k = 30
100 µm
Lowest among nine sampled points only.
Warmer colors indicate higher modeled peak die temperature; none of the grid values is experimental.
17

## Slide 18
The thermal trend: thin BLT and higher k both help
RESULTS / PARAMETER SENSITIVITY
Source: project Icepak/MAPDL numerical results; 23 Oct 2026 evidence freeze. Model-specific, not experimental data.
75
86
98
109
120
100 µm
250 µm
400 µm
k = 15
k = 21
k = 30
Isolated contrasts
−10.719 °C
250 → 100 µm
at k = 21
−5.318 °C
k: 21 → 30
at 250 µm
Trend is bounded to k = 15–30 W/(m·K) and BLT = 100–400 µm; not a continuous global optimum.
18

## Slide 19
Does the shortlist persist at 88.22% retention?
RESULTS / CONTACT ROBUSTNESS
Team's recovered four-case Icepak results; retained area motivated by Yi et al., Microelectron. Reliab. 166 (2025), 115607. DOI: 10.1016/j.microrel.2025.115607.
21 / 250
full
93.3°
21 / 250
88.22%
93.7°
30 / 250
88.22%
88.3°
30 / 100
88.22%
80.7°
80.650 °C
Thin/high-k remains thermally strongest of the four tested cases.
Fixed idealized retained footprint—not a physical peel/delamination model.
The four-case result includes recovery of an initially interrupted solver run without parameter changes.
19

## Slide 20
Thermal fields transferred into a common structural model
METHODS / MECHANICAL MODEL
Source: project Icepak/MAPDL numerical results; 23 Oct 2026 evidence freeze. Model-specific, not experimental data.
Icepak fields
9 independent solved
k–BLT conditions
Reduced handoff
Die-class and layer-
average temperatures
MAPDL quarter model
SOLID186, fully bonded
one-way response
Compare outputs
TIM stress & strain;
lid-top warpage
Reference carbon mechanics held fixed: E = 1.0 MPa; ν = 0.49; CTE = 180 ppm/K
20

## Slide 21
Mechanical-property sensitivity: warpage is not enough
RESULTS / EFFECTIVE PROPERTIES
Source: project Icepak/MAPDL numerical results; 23 Oct 2026 evidence freeze. Model-specific, not experimental data.
Warpage for two different thermal designs
Lower modulus
17.38
16.21
Reference modulus
19.01
17.16
Higher modulus
19.87
17.59
k = 21, 250 µm
k = 30, 100 µm
+27.25% stress
Higher-modulus pair
+27.32% strain
Warpage improved while average stress and strain worsened.
21

## Slide 22
Mesh refinement: trust the averages, not peak stress
VALIDATION / LIMITS
Source: project Icepak/MAPDL numerical results; 23 Oct 2026 evidence freeze. Model-specific, not experimental data.
Mean stress
0.59%
Mean strain
1.96%
Lid warpage
0.04%
Local peak stress
50.20%
Absolute intermediate-to-fine changes; peak stress lacks mesh convergence.
The report does not use pointwise peak stress as a quantitative failure or fatigue criterion.
22

## Slide 23
A fairer mechanical comparison: nine matched cases
METHODS / DESIGN OF EXPERIMENTS
Source: project Icepak/MAPDL numerical results; 23 Oct 2026 evidence freeze. Model-specific, not experimental data.
100 µm
250 µm
400 µm
k = 15
85.5°
100.3°
114.4°
k = 21
82.6°
93.3°
103.5°
k = 30
80.5°
88.0°
95.2°
9 thermal
fields
9 matched
mechanical runs
Same modulus, CTE, ν and structural protocol.
Conductivity and BLT change; each corresponding solved thermal condition feeds the same MID-property model.
23

## Slide 24
Average TIM stress is lowest at 250 µm
RESULTS / MATCHED MECHANICS
Source: project Icepak/MAPDL numerical results; 23 Oct 2026 evidence freeze. Model-specific, not experimental data.
100 µm
250 µm
400 µm
k = 15
0.012094
0.012014
0.013286
k = 21
0.011960
0.011339
0.012153
k = 30
0.011866
0.010841
0.011306
STRESS MINIMUM
0.010841
MPa
k = 30
BLT = 250 µm
Within sampled, assumed model.
At every k in {15, 21, 30} W/(m·K), the sampled 250-µm BLT minimizes mean stress and strain.
24

## Slide 25
Mean TIM strain confirms the intermediate-BLT minimum
RESULTS / MATCHED MECHANICS
Team's nine matching Icepak-to-MAPDL MID-model simulations (dimensionless strain shown as %).
1.08
1.16
1.23
1.30
1.38
100 µm
250 µm
400 µm
k = 15 W/(m·K)
k = 21 W/(m·K)
k = 30 W/(m·K)
A matched result
1.1076%
Lowest sampled equivalent elastic strain at k = 30 W/(m·K), BLT = 250 µm.
At every sampled conductivity, the 250-µm case minimizes mean stress AND mean strain.
25

## Slide 26
Thinner BLT improves modeled warpage
RESULTS / MATCHED MECHANICS
Source: project Icepak/MAPDL numerical results; 23 Oct 2026 evidence freeze. Model-specific, not experimental data.
16.0
18.0
20.0
22.0
24.0
100 µm
250 µm
400 µm
k = 15
k = 21
k = 30
k = 30 W/(m·K)
17.155 µm
Lowest modeled lid warpage among nine cases.
But mean TIM stress is not minimized at 100 µm.
26

## Slide 27
Holding conductivity fixed reveals the trade-off
RESULTS / CONTROLLED COMPARISON
Source: project Icepak/MAPDL numerical results; 23 Oct 2026 evidence freeze. Model-specific, not experimental data.
−7.571 °C
Peak temperature
250 → 100 µm
−2.47%
Lid warpage
250 → 100 µm
+9.46%
Mean TIM stress
250 → 100 µm
All three changes occur at fixed k = 30 W/(m·K).
Mean equivalent elastic strain rises by 10.86% when BLT falls from 250 to 100 µm.
27

## Slide 28
The sampled thermal–mechanical decision map
RESULTS / MULTI-OBJECTIVE COMPARISON
Source: project Icepak/MAPDL numerical results; 23 Oct 2026 evidence freeze. Model-specific, not experimental data.
0.0104
0.0112
0.0121
0.0129
0.0138
78
88
98
108
118
100 µm
250 µm
Peak die temperature [°C]
Two priorities
THERMAL PRIORITY
30 W/m·K, 100 µm
LOWER TIM STRESS
30 W/m·K, 250 µm
Discrete sampled operating points, not a fitted Pareto frontier or globally proven optimum.
28

## Slide 29
Engineering recommendation: two candidates
DECISION
Source: project Icepak/MAPDL numerical results; 23 Oct 2026 evidence freeze. Model-specific, not experimental data.
THERMAL STRETCH
k = 30 W/(m·K) | BLT = 100 µm
Clean Tmax
80.455 °C
88.22% Tmax
80.650 °C
Mean stress
0.011866 MPa
Mean strain
1.2279%
Lid warpage
17.155 µm
Choose when modeled die temperature and warpage dominate.
LOWER-STRESS
k = 30 W/(m·K) | BLT = 250 µm
Clean Tmax
88.026 °C
88.22% Tmax
88.295 °C
Mean stress
0.010841 MPa
Mean strain
1.1076%
Lid warpage
17.590 µm
Choose when mean TIM stress and strain dominate.
Different scenario models: retained-area thermal runs and fully bonded mechanical analyses are not co-simulated.
29

## Slide 30
Executive takeaway
THE ENGINEERING ANSWER
Source: project Icepak/MAPDL numerical results; 23 Oct 2026 evidence freeze. Model-specific, not experimental data.
One package. Two valid priorities.
80.455 °C
Lowest modeled die temperature
k = 30 W/(m·K), BLT = 100 µm
0.010841 MPa
Lowest sampled mean TIM stress
k = 30 W/(m·K), BLT = 250 µm
9.46%
Stress penalty for thinner BLT
250 → 100 µm at fixed k = 30
Higher conductivity helps broadly; installed thickness creates the sampled thermal–mechanical trade-off.
30

## Slide 31
Scientific boundaries: what we cannot claim
LIMITATIONS
Reliability model limitations: Subramanian et al. (2019), DOI: 10.1115/1.4042805; Zhao et al., Int. J. Heat Mass Transfer 140 (2019), 705-716. DOI: 10.1016/j.ijheatmasstransfer.2019.06.045.
Thermal boundary
Fixed 25 °C cold-plate surface; coolant flow not resolved.
Contact-loss geometry
Illustrative ideal blockage; not measured void shapes or a damage-growth law.
Mechanical response
Assumed linear effective properties and fully bonded one-way thermal handoff.
Reliability prediction
No validated fatigue, pump-out, delamination or failure criterion; peak stress unconverged.
Use the results for relative design screening, not measured product lifetime or manufacturing qualification.
31

## Slide 32
A realistic path to reliability qualification
FUTURE WORK / INDUSTRIAL ADOPTION
Qualification directions motivated by cited TIM reliability and contact-resistance literature.
01
Material coupons
Measure through-plane k, compressed BLT, anisotropy, temperature dependence.
02
Interface tests
Measure contact resistance vs. pressure and temperature; retention maps.
03
Coupled packaging
Introduce contact pressure, deformation, interface gaps and calibrated constitutive laws.
04
Reliability tests
Thermal cycling, pump-out, adhesion, C-SAM, delamination and fatigue criteria.
No lifetime extension or industrial product readiness has been established by this simulation alone.
Qualification approach: Due & Robinson (2013), DOI: 10.1016/j.applthermaleng.2012.06.013; Zhao et al., Int. J. Heat Mass Transfer 140 (2019), 705-716. DOI: 10.1016/j.ijheatmasstransfer.2019.06.045.
32

## Slide 33
Take-home messages
CONCLUSION
Source: project Icepak/MAPDL numerical results; 23 Oct 2026 evidence freeze. Model-specific, not experimental data.
01
Do not optimize k in isolation
BLT, contact retention and hotspot location control the relevant thermal path.
02
Topology matters
Equal 64.82% retained area produced very different modeled thermal outcomes.
03
The best thermal point is not the lowest-stress point
At k = 30, 100 µm cools best; 250 µm minimizes sampled mean stress/strain.
Deliverable: a traceable two-candidate design window for experimental qualification.
33

## Slide 34
Literature and evidence references
REFERENCES
Prasher, R. S. (2006). Thermal interface materials: Historical perspective, status and future directions. Proc. IEEE. DOI: 10.1109/JPROC.2006.879796
Due, J., & Robinson, A. J. (2013). Reliability of thermal interface materials: A review. Applied Thermal Engineering. DOI: 10.1016/j.applthermaleng.2012.06.013
Zhao, J.-W. et al. (2019). Effects of surface roughness, temperature and pressure on interface thermal resistance. IJHMT. DOI: 10.1016/j.ijheatmasstransfer.2019.06.045
Li, J. et al. (2023). Compliance-tunable TIMs based on vertically oriented carbon fiber arrays. Composites Science and Technology. DOI: 10.1016/j.compscitech.2023.109948
Yi, M. et al. (2025). FCBGA package with vertical-aligned carbon-fiber thermal pad. Microelectronics Reliability. DOI: 10.1016/j.microrel.2025.115607
Wen, J. et al. (2026). Indium-based self-confining metal foam TIMs for large-die FCBGA. IJTS. DOI: 10.1016/j.ijthermalsci.2025.110432
Subramanian, V. et al. (2019). Mechanical characterization of TIMs and its challenges. Journal of Electronic Packaging. DOI: 10.1115/1.4042805
Du, W. et al. (2026). TIM thermal-mechanical reliability and coverage degradation prediction. Microelectronics Reliability. DOI: 10.1016/j.microrel.2026.116180
Yenigun, O. et al. (2026). Coupled thermal and mechanical analysis of TIMs in electronic packaging. IEEE TCPMT. DOI: 10.1109/TCPMT.2025.3633174
Project numerical source: EPTC team report and frozen Icepak/MAPDL exports; 23 Oct 2026.
34

## Slide 35
Backup: complete nine-case comparison
APPENDIX / NUMERICAL DATA
Source: project Icepak/MAPDL numerical results; 23 Oct 2026 evidence freeze. Model-specific, not experimental data.
k [W/mK]
BLT [µm]
Tmax [°C]
Mean VM [MPa]
Strain [%]
Warp [µm]
Case
15
100
85.490
0.012094
1.2568
18.611
15
250
100.323
0.012014
1.2296
20.948
15
400
114.389
0.013286
1.3535
23.503
21
100
82.625
0.011960
1.2400
17.778
21
250
93.344
0.011339
1.1594
19.012
21
400
103.544
0.012153
1.2369
20.496
30
100
80.455
0.011866
1.2279
17.155
LOWEST T
30
250
88.026
0.010841
1.1076
17.590
LOWEST σ
30
400
95.194
0.011306
1.1498
18.293
35